## Slide 1: Chapter 3 Floorplanning
108062135 呂佳恩

## Slide 2: Floorplanning
Input :
  Hard blocks (rigid blocks) : Blocks with well-defined areas and shapes
  Soft blocks (flexible blocks) : Blocks with approximate areas and no particular shapes
  Netlist : Specification about the connections between the blocks
Goal :
  Find locations for all blocks so that blocks do not overlap
  Consider shapes, dimensions of soft blocks and pin locations of all the blocks
  Minimize area
  Reduce wirelength for critical nets
  Maximize routability
  Address thermal hotspots, power supply noise

## Slide 3
Constraints:
  Fixed outline
  Preplaced blocks
  Alignment problems
Floorplanning

## Slide 4: Floorplan Elements
Leaf block (cell/module) : a block at the lowest level of the hierarchy, it does not contain any other block.
Composite block (cell/module) : a block that is composed of either leaf blocks or lower-level composite blocks.
The whole IC is the highest-level composite block

## Slide 5: Slicing Floorplan Slicing Tree
A composite block’s subblocks are obtained by a horizontal or vertical bisection/slice of the composite block
Slicing floorplans can be represented by a slicing tree.
A slicing tree could also be called a floor plan of order 2
In a slicing tree, all blocks except for the top level block have a parent, and all composite blocks have children

## Slide 7: Floorplanning
Rectangular dissection : Subdivision of a given rectangle by a finite number of horizontal and vertical line segments into a finite number of non-overlapping rectangles.
Slicing structure : a rectangular dissection that can be obtained by repetitively subdividing rectangles horizontally or vertically
Skewed slicing tree: One slicing tree which no node and its right child are the same

## Slide 8: Stockmeyer Algorithm
Input :
  A slicing floorplan
Output :
  An orientation of the blocks in the floorplan so that the overall floorplan area is minimized.
Usage :
  Mostly used in post-process of the given slicing floorplan to further optimize the area objective.
For a non-slicing floorplan, it is proved that the optimal orientation problem is NP-complete

## Slide 9: Stockmeyer algorithm
Rough Idea :
  traverse the internal nodes of the slicing tree in bottom up so that we compute the candidate dimensions of each internal node.
  Traverse the tree in top down fashion to select the dimensions for the internal nodes as well as the orientation of the leaf nodes, based on the decision made by the parent node.

## Slide 10: Stockmeyer algorithm
Vertical Slice :
  Suppose we have two children that are leaves ( bottom up ), we denote the dimensions of the nodes as left (wl, hl), right child (wr, hr)
  Dimensions of the left and the right child are sorted so that the width is increasing and the height is decreasing
  The resulting dimension after the merging is (wl + wr , max{hl, hr})
  If hl > hr, we merge the second dimension of the left child and the first dimension of the right child
  If hl < hr, we merge the first dimension of the left child and the second dimension of the right child
  If hl = hr, we merge the second dimension of the left child and the second dimension of the right child
  The merging is ended when we reach the end of the dimension list for either the left or the right child

## Slide 11: Stockmeyer algorithm
Horizontal Slice :
  Suppose we have two children that are leaves ( bottom up ), we denote the dimensions of the nodes as left (wl, hl), right child (wr, hr)
  Dimensions of the left and the right child are sorted so that the width is decreasing and the height is increasing
  The resulting dimension after the merging is (max{wl,wr}, hl + hr)
  If hl > hr, we merge the second dimension of the left child and the first dimension of the right child
  If hl < hr, we merge the first dimension of the left child and the second dimension of the right child
  If hl = hr, we merge the second dimension of the left child and the second dimension of the right child
  The merging is ended when we reach the end of the dimension list for either the left or the right child

## Slide 12: Stockmeyer Algorithm example

## Slide 13: Width, height = {(2,4), (1,3), (3,3), (3,5), (3,2), (5,3), (1,2), (2,4)}.
Visit node a -> cut Vertical -> left child(5(3,2)), right child(1(2,4))
L = {(2, 3), (3, 2)}
R = {(2, 4), (4, 2)}
Join L1, R1 -> (2 + 2,max{3, 4}) = (4,4) ->maximum from R-> Join L1, R2
Join L1, R2 -> (2 + 4,max{3, 2}) = (6,3) ->maximum from L -> Join L2 R2
Join L2, R2 ->(3 + 4,max{2, 2}) = (7, 2) ->reach end
Result dimensions {(4, 4), (6, 3), (7, 2)}.
L = {(2, 3), (3, 2)} R = {(2, 4), (4, 2)}
L = {(2, 3), (3, 2)} R = {(2, 4), (4, 2)}
L = {(2, 3), (3, 2)} R = {(2, 4), (4, 2)}

## Slide 14: Stockmeyer Algorithm example

## Slide 15: Width, height = {(2,4), (1,3), (3,3), (3,5), (3,2), (5,3), (1,2), (2,4)}.
Visit node b -> cut Horizontal -> left child(8(2,4)), right child(2(1,3))
L = {(4, 2), (2, 4)}
R = {(3, 1), (1, 3)}
Join L1, R1 -> (max{4, 3},2 + 1) = (4, 3)->maximum from L-> Join L2, R1
Join L2, R1 -> (max{2, 3},4 + 1) = (3, 5)->maximum from R -> Join L2 R2
Join L2, R2 -> (max{2, 1},4 + 3) = (2, 7)->reach end
Result dimensions {(4, 3), (3, 5), (2, 7)}.
L = {(4, 2), (2, 4)} R = {(3, 1), (1, 3)}
L = {(4, 2), (2, 4)} R = {(3, 1), (1, 3)}
L = {(4, 2), (2, 4)} R = {(3, 1), (1, 3)}

## Slide 16: Stockmeyer Algorithm example

## Slide 17: Visit C
Cut vertical->left child a, right child b
L = {(4, 4), (6, 3), (7, 2)}
R = {(2, 7), (3, 5), (4, 3)}
Join L1, R1 -> (4 + 2,max{4, 7}) = (6, 7) ->maximum from R -> Join L1, R2
Join L1, R2 -> (4 + 3,max{4, 5}) = (7, 5) ->maximum from R -> Join L1, R3
Join L1, R3 -> (4 + 4,max{4, 3}) = (8, 4) ->maximum from L -> Join L2, R3
Join L2, R3 -> (6 + 4,max{3, 3}) = (10, 3) ->R=L -> reach End
Result dimensions {(6, 7), (7, 5), (8, 4), (10, 3)}.
L = {(4, 4), (6, 3), (7, 2)} R = {(2, 7), (3, 5), (4, 3)}
L = {(4, 4), (6, 3), (7, 2)} R = {(2, 7), (3, 5), (4, 3)}
L = {(4, 4), (6, 3), (7, 2)} R = {(2, 7), (3, 5), (4, 3)}
L = {(4, 4), (6, 3), (7, 2)} R = {(2, 7), (3, 5), (4, 3)}

## Slide 18: Stockmeyer Algorithm example

## Slide 19: Visit D, Width, height = {(2,4), (1,3), (3,3), (3,5), (3,2), (5,3), (1,2), (2,4)}.
Cut vertical->left child c, right child 4
L = {(6, 7), (7, 5), (8, 4), (10, 3)}
R = {(3, 5)(5, 3)}
Join L1, R1 -> (6 + 3,max{7, 5}) =(9, 7) ->maximum from L -> Join L2, R1
Join L2, R1 -> (7 + 3,max{5, 5}) = (10, 5)->R=L-> Join L3, R2
Join L3, R2 -> (8 + 5,max{4, 3}) = (13, 4)->maximum from L -> Join L4, R2
Join L4, R2 ->(10 + 5,max{3, 3}) =(15, 3). ->R=L -> reach End
Result dimensions {(9, 7), (10, 5), (13, 4), (15, 3)}.
L = {(6, 7), (7, 5), (8, 4), (10, 3)}
R = {(3, 5)(5, 3)}
L = {(6, 7), (7, 5), (8, 4), (10, 3)}
R = {(3, 5)(5, 3)}
L = {(6, 7), (7, 5), (8, 4), (10, 3)}
R = {(3, 5)(5, 3)}
L = {(6, 7), (7, 5), (8, 4), (10, 3)}
R = {(3, 5)(5, 3)}

## Slide 20: Stockmeyer Algorithm example

## Slide 21: Visit f
L = {(9, 7), (10, 5), (13, 4), (15, 3)}
R = {(3, 5)(5, 3)}
Result dimensions {(12, 7), (13, 5), (18, 4), (20, 3)}.
Visit e
L = {(3, 3)}
R = {(2, 1)(1, 2)}
Result dimensions {(3, 4)}.
Visit g
L = {(3, 4)}
R = {(20, 3), (18, 4), (13, 5), (12, 7)}
Result dimensions {(20, 7), (18, 8), (13, 9), (12, 11)}.

## Slide 22: After visiting node G
Resulting Dimensions are {(20, 7), (18, 8), (13, 9), (12, 11)}.
Calculate the minimum area floor plan
13 x 9 = 117 is the minimum area

## Slide 23: Top down to fine the optimal orientation
Node G : Choose (13, 9) coming from joining (3,4) and (13, 5)
Thus, node e is (3,4) node f is (13,5)

## Slide 24: Top down to fine the optimal orientation
Node E : From Node G we know that Node E is (3,4)
This comes from joining (3,3) and (2,1)
We can see that the best orientation for
Block 3 is (3,3) and block 7 is (2,1)
Block 7 is rotated

## Slide 25: Stockmeyer Algorithm example

## Slide 26: Top down to fine the optimal orientation
Node f : From Node G we know that Node E is (13,5)
This comes from joining (10,5) and (3,5)
Node d is (10,5) and optimal orientation of
Block 6 is (3,5)
Block 6 is rotated

## Slide 27: Stockmeyer Algorithm example

## Slide 28: Top down to fine the optimal orientation
Node d : we know from Node f that Node d is (10,5)
This comes from joining (7,5) and (3,5)
Node c is (7,5) and optimal orientation for
block 4 is (3,5)

## Slide 29: Top down to fine the optimal orientation
Node c : we know from Node d that Node c is (7,5)
This comes from joining (4,4) and (3,5)
Node a is (4,4) and Node b is (3,5)

## Slide 30: Top down to fine the optimal orientation
Node a : we know from Node c that Node a is (4,4)
This comes from joining (2,3) and (2,4)
Optimal orientation of block 5 is (2,3)
Optimal orientation of block 1 is (2,4)
Block 5 is rotated

## Slide 31: Stockmeyer Algorithm example

## Slide 32: Top down to fine the optimal orientation
Node b : we know from Node c that Node a is (3,5)
This comes from joining (2,4) and (3,1)
Optimal orientation of block 8 is (2,4)
Optimal orientation of block 2 is (3,1)
Block 2 is rotated

## Slide 33: Before, after
4 blocks are rotated
Area reduced from 15x12 to 13x9

## Slide 34: Conclusion
The Stockmeyer algorithm can improve the area significantly, or not at all, depending on the original placement and the critical path
Critical path is the longest path in the circuit and limits the clock speed.
If the Critical path is already minimized, then the area will stay the same.
Wire routing is a significant problem that we have to consider in a real world situation that this algorithm does not take into account

## Slide 35: ILP Floorplanning Algorithm
ILP – Integer Linear Programming
How is ILP applied to floor planning?
  The constraints specifying a feasible floor plan are described by a set of mathematical equations
  Can use commercial ILP solvers

## Slide 36: Problem Formulation
Modules of the problem make up the group S
Modules can be rigid or flexible
The original algorithm can handle flexible modules, however, it adds complexity to the problem
The textbook assumes the modules are all rigid for the following.
Rigid Block – Blocks with well-defined areas and shapes
Soft Block – Blocks with approximate areas and no particular shapes

## Slide 37: Problem Formulation
Widths and heights of modules are known
Suppose for module i, width and height are denoted as pair )
And the bottom left corner of the module is denoted as )

## Slide 38: Module i is to the left of Module j

## Slide 39: Module i is below Module j

## Slide 40: Module i is to the right of Module j

## Slide 41: Module i is above Module j

## Slide 42: Relative positions of modules
Relative positions of 2 modules i and j are represented/governed by
the following 4 equations

## Slide 43: Equations to be satisfied (example 1)

## Slide 44: Equations to be satisfied (example 2)

## Slide 45: Small conclusion
If we don’t want the Modules to overlap, one of the 4 following equations have to be satisfied

## Slide 46: How to represent?
We introduce a pair of binary variables () associated with each pair of modules
= 0 and = 0 implies that module i is left of j
= 0 and = 1 implies that module i is below of j
= 1 and = 0 implies that module i is right of j
= 1 and = 1 implies that module i is above of j

## Slide 47: ILP floorplanning
To enforce that no two modules overlap, we introduce two more variables W and H, representing the width and height of the entire floor respectively. If it is not given, we could use the width, height sum of all blocks to be W, H.
After introducing W and H, combined with the pair of binary variables (), we rewrite the four limitations.

## Slide 48: Rewriting limitations
The limitations are rewritten as the following
We can find out that, according to the placement of two modules, one of the four equations will be used to reinforce the placement, while the other three conditions will be always true.

## Slide 49: Example, suppose = 0 and = 1
The equations will be as the following

## Slide 50: Linear programming Formulation
Assumption: one dimension of the chip (W) is fixed.
  This is done to linearize the problem, just have to optimize one variable
Case 1: All modules are rigid and have fixed orientation (no rotation)
Constraints
  No two modules overlap
  Each module is enclosed within the floorplan enveloping rectangle of width W and height Y
  We place all modules and the floor in the first quadrant
Objective: Since W is fixed, objective would be to minimize Y, the height of the floor plan

## Slide 51: Linear Programming Formulation
We have the following inequations that we have to satisfy

## Slide 52: Linear programming Formulation
Case 2: suppose the modules are Rigid, but rotation is allowed
We need to add another 0-1 integer variable to record whether the block is rotated or not!
Introduce
  = 0 if the block is not rotated
  = 1 if the block is rotated
We have to change the inequations to account for rotating!!

## Slide 53: Linear Programming Formulation
Introduce
  = 0 if the block is not rotated
  = 1 if the block is rotated
W and H has to be replaced by M since we don’t know which direction the block will be placed
  M can be set to max(W,H) or W+H
The number of equations remains unchanged, however, the number of 0-1 integer variables have increased by n(number of modules)

## Slide 54: Example
Problem: Formulate the ILP floorplanning for the following instances, The desired aspect ration is 1
  The dimension of the fixed modules are given as (width, height)
  There are four fixed modules, m1(4, 5), m2(3, 7), m3(6, 4), and m4(7, 7). Rotation is not allowed.
  The aspect ration = 1 helps simplify the problem

## Slide 55: Step 1
We obtain the list of continuous and integer variables as follows
Calculate the upper bound as following

## Slide 56
We then try to minimize y∗,
following the non-overlap constraints, we obtain

## Slide 57
Following the variable type constraints, we obtain
Following the chip width constraints:

## Slide 58
Following the height constraints:
After using a commercial solver, we obtain the following floorplan

## Slide 59: Sequence pair Algorithm
Sequence pair is an easy representation of non-slicing floorplans of Modules
  Similar to the Polish algorithm
  The Polish algorithm is used for slicing floorplans
Use Simulated Annealing to find a good sequence-pair

## Slide 60: Floor plan to Sequence pair (Gridding)
Two types of sequence pairs
  Up-right
  Down-left
Up-right Sequence pair
  Start from the bottom left corner of a module until the upper right corner of the floor plan is reached. Draw vertical lines going up and horizontal lines going right in an alternate fashion so that the lines for all module do not cross
Down-left Sequence pair
  Start from the upper left corner of a module until the bottom right corner of the floor plan is reached. Draw vertical lines going down and horizontal lines going left in an alternate fashion so that the lines for all module do not cross

## Slide 61: Up right sequence pair – Positive step line
The order among the lines from left
to right at the bottom left corner would be
the Positive step line sequence.
Positive step line sequence would be
ecadfb

## Slide 62: Down-left sequence pair - Negative step line
The order among the negative step lines from
bottom to top form the negative step line sequence
Negative step line sequence
fcbead

## Slide 63: Benefits
Sequence pairs offer an advantages similar as the Polish expression, when used together with simulated Annealing
  It provides efficient exploration of the solution space via local search
  Polynomial time evaluation of a candidate solution
  Author also shows that the solution space defined by sequence pair is called P-admissible, which in that situation always exists an optimal solution to the problem

## Slide 64: P-admissible
The solution space that satisfies the following requirements are called P-admissible
  The solution space is finite
  Every solution is feasible
  Realization of a code is possible in polynomial time
  There exists a code which corresponds to one of the optimal solution
Theorem:
  The set of all sequence pairs is a p-admissible solution space, More precisely , it consists of sequence pairs, each of which can be mapped to a packing in O , where at least one of which corresponds to one of the optimal solutions

## Slide 65: Geometric Info of sequence pair
Given a sequence pair (P, N), module a, b is a part of the set of blocks
a is right to b iff a is after b in both P and N
a is left to b iff a is before b in both P and N
a is above b iff a is before b in P and a is after b in N
a is below b iff a is after b in P and a is before b in N

## Slide 66: Moves to optimize
M1 is swapping a random pair of modules in the first sequence
M2 is swapping a random pair of modules in both sequences
M3 is rotating a randomly selected module by 90 degrees

## Slide 67: Example
Consider the following sequence pair SP1 = (17452638, 84725361).
The (width, height) of the modules 1 through 8 are {(2,4), (1,3), (3,3), (3,5), (3,2),(5,3), (1,2), (2,4)}.
Steps:
  Draw the Horizontal and vertical constraint graphs
  Find out the minimum area of the non-slicing floorplan\
    The longest s-t path from horizontal and vertical
  Draw out the corresponding non-slicing floorplan, find the location of the lower left corner of each module

## Slide 68: SP1 = (17452638, 84725361).
Using the geometric info provided by both sequences, we obtain the chart

## Slide 69: SP1 = (17452638, 84725361)
Then we try to map the sequence onto a grid marked as the following

## Slide 70: SP1 = (17452638, 84725361) (Horizontal)
The block would be placed on the intersection of the values, and add source to the left and target to the right

## Slide 71: SP1 = (17452638, 84725361) (Horizontal)
We then connect the blocks

## Slide 72: SP1 = (17452638, 84725361) (Vertical)
Add source to the bottom and the target on top

## Slide 73: SP1 = (17452638, 84725361)
Add values of the width/height on the Horizontal/Vertical constraint graph, and find the longest path from s->t, it would be used to calculate the minimum area

## Slide 74: SP1 = (17452638, 84725361)
We then calculate the longest path lengths for the modules in the Horizontal constraint graph and vertical constraint graph
Area : 11x 15

## Slide 75: Perform Moves
Perform M1 move which swaps module 1 and 3 are swapped in the first(positive) sequence
SP1 = (17452638, 84725361) =>> SP2= (37452618, 84725361).

## Slide 76: SP2= (37452618, 84725361).

## Slide 77: SP2= (37452618, 84725361)
Calculate the minimum area
Area = 13x14

## Slide 78: SP1 ->> SP2
Area : 11x 15
Area = 13x14

## Slide 79: Perform Move
Swap Modules 4 and 6 in both sequences
SP2= (37452618, 84725361) -> SP3 =(37652418, 86725341)

## Slide 80: SP3 =(37652418, 86725341)

## Slide 81: SP3 =(37652418, 86725341)
Area = 13x12

## Slide 82: SP1 ->> SP2 ->> SP3
Area : 11x 15
Area = 13x14
Area = 13x12